## Slide 1: K Street NW Traffic Analysis

## Slide 2
Outline
Data Collection
Building a Calibrated Model
Analysis of Existing Network
Define the Two Initial Build Alternatives
Alternatives Analysis
Next Steps
Hybrid Alternative
Introduction
Project Schedule
Process Overview

## Slide 3
Introduction
The K Street Transitway is a priority project that will reconfigure one of the District's major east-west corridors, K Street NW, with vast improvements to benefit bus riders, motorists, cyclists, and pedestrians.
DDOT’s Project Goals:
Provide safe and reliable access for the largest number of people through the downtown corridor through prioritizing transit, pedestrian, and bicycle modes.
By focusing on dedicated and protected space for transit riders and cyclists, make it easier, faster, and more reliable for more people to get safely to and through downtown DC.
Bring mobility benefits to the greatest number of people by giving dedicated space to buses and enhancing pedestrian and bicycle infrastructure.
People in buses, on foot, and on bikes make up the majority of current – and future – K Street travelers.

## Slide 4
Milestone Schedule
Traffic Analysis
Fall 2019 – Summer 2020
30% Design
Fall 2019 – Spring 2020
Final Design
Fall 2020 – Fall 2021
Construction
Start Early 2022

## Slide 5
Traffic Analysis Process
Data Collection
Building a Calibrated Model
Analysis of Existing Network
Define the Two Initial Build Alternatives
Alternatives Analysis
Hybrid Alternative
Next Steps

## Slide 6: Data Collection

## Slide 7: Data Collection Plan

## Slide 8: Data Collection
Heavy pedestrian traffic outside the Farragut North Metrorail Station
Sporadic use of service lanes by bicycles
Bus bunching, Eastbound at 16th Street NW
Challenging egress from parking garages and navigating service lanes (PM) [note illegally parked FedEx truck in service lane access break]
Right-of-way confusion entering service lanes (AM)

## Slide 9: Data Collection
Chart: 
AM | 636 | 1967 | 2873 | 2659 | 2978 | 5709 | 3787 | 1396 | 2876 | 1776 | 2890 | 1199 | 728 | 751 | 623
PM | 622 | 1496 | 1777 | 2302 | 3175 | 5141 | 2456 | 1185 | 2088 | 1974 | 2391 | 911 | 649 | 562 | 628
1,680
1,516
170
160
1,471
713
761
923
491
456
Total Pedestrian Crossings (AM and PM Peak Hour)*
*Traffic data collected on December 4, 2019
941
749
##
##
AM PM Maximum Hourly Pedestrian Volume Across a Single Leg of the Intersection (pedestrian symbol scaled to represent magnitude of crossing volume)

## Slide 10
M
Bus Stop Locations on K Street NW Mainline
K+20th
K+19th
K+16th
K+14th
K+13th
K+15th
K+18th
K+19th
K+16th
K+14th
K+13th
K+18th
K+15th
K+11th
Average Dwell Time
21 sec
EASTBOUND
AM Peak
PM Peak
22 sec
WESTBOUND
Average Dwell Time
17 sec
AM Peak
PM Peak
22 sec
K+20th
K+CT
K+CT/17th
Hot Spots with High Average Dwell Time
K+20th
42 sec
AM Peak
K+CT, EB
40 sec
AM Peak
32 sec
AM Peak
K+CT, WB
* Transit dwell time distributions derived from WMATA AVL data.
* PM peak period average dwell times were consistent with one another, hot spots not identified.
Bus Average Dwell Time

## Slide 11: Traffic Simulation Model

## Slide 12
Simulates the presence and behavior of each individual user in the network
Records performance metrics for all network users and the network as a whole
Model is calibrated to real-world conditions
Enables the analysis of build alternatives in a future condition to inform design
What is Traffic Simulation Modeling?

## Slide 13
Understand modal interaction
Determine travel times
Calculate transit dwell time changes
Simulate driving behaviors
Replicate real-world congestion
Benefits of Traffic Modeling

## Slide 14
Accounting for trip diversions
K St NW
I St NW
H St NW
21st St NW
20th St NW
19th St NW
18th St NW
Original Trip
Trip Diversion
Capturing surrounding network congestion
M
L
K
I
H
22
21
20
19
18
CT
17
16
15
VT
14
13
12
Study Area
Simulating prohibited curbside activity
Loading/Unloading
Shortcomings of Traffic Modeling

## Slide 15
Building a Calibrated Model
Calibration is the adjustment of model parameters to represent real-world conditions
Corridor Travel Time
Vehicular Throughput
Queues & Bottlenecks
34
478
6
54
710
0
3
76
737
1
1
604
1
Traffic Counts
Simulated Counts
=

## Slide 16: Analysis of Existing Network
Traffic operations reported from calibrated Vissim traffic model

## Slide 17: Travel Time
AM Peak
PM Peak
7:08
7:33
12:56
15:08
AM Peak
7:21
9:37
12:31
14:03
Eastbound Travel Time
Westbound Travel Time
Chart: 
| AM, Eastbound | PM, Eastbound | AM, Westbound | PM, Westbound
Vehicle | 0.29722 | 0.31458 | 0.30625 | 0.40069
Bus | 0.53889 | 0.63056 | 0.52153 | 0.58542
EASTBOUND
WESTBOUND
EASTBOUND
WESTBOUND
PM Peak
Notes: Vehicles Existing Conditions AM – Average eastbound travel time = 7:08, Average westbound travel time = 7:21
Transit Existing Conditions AM – Average eastbound travel time = 12:56, Average westbound travel time = 12:31 (includes dwell time)
Vehicles Existing Conditions PM – Average eastbound travel time = 7:33, Average westbound travel time = 9:37
Transit Existing Conditions PM – Average eastbound travel time = 15:08, Average westbound travel time = 14:03 (includes dwell time)

## Slide 18: Intersection Delay
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Connecticut Avenue NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
Chart: 
| 22nd Street NW | 21st Street NW | 20th Street NW | 19th Street NW | 18th Street NW | Connecticut Avenue NW | 17th Street NW (east) | 16th Street NW | 15th Street NW (west) | Vermont Avenue NW | 14th Street NW | 13th Street NW | 12th Street NW | 11th Street NW | 10th Street NW | 9th Street NW
AM | 8.7034 | 20.4828 | 25.7391 | 27.3426 | 24.8024 | 35.023 | 29.0152 | 29.8908 | 38.2436 | 36.3493 | 52.3521 | 24.5147 | 38.7646 | 20.3929 | 20.5593 | 8.2256
PM | 32.8185 | 43.7016 | 20.0303 | 25.2323 | 20.9682 | 45.656 | 26.484 | 25.3506 | 45.5136 | 50.0182 | 43.5167 | 25.0805 | 32.7807 | 20.8529 | 21.4083 | 13.4641
Delay [seconds]
AM / PM
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor
AM
PM
Intersection Performance
Notes: Existing LOS AM/PM
Pie chart summarizing AM / PM - # of intersections in each category.
Key for coloring of circles.

## Slide 19: Approach Delay
K Street NW and
Connecticut Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
15th Street NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
Vermont Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
14th Street NW (east)
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
12h Street NW
AM
PM
AM
PM
AM
PM
K Street NW and
21st Street NW
AM - ML
PM - ML
AM
PM
AM
PM
AM
PM
AM - SL
PM - SL
*ML: Mainline K Street NW (from tunnel) *SL: Service Lane (from Washington Circle)
AM
PM
Intersection Performance
Approach Performance
AM
PM
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor

## Slide 20
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Connecticut Avenue NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
AM Peak
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
Connecticut Avenue NW
7 mph
4 mph
4 mph
6 mph
6 mph
5 mph
6 mph
4 mph
Slowest Speeds along Corridor
SPEED LIMIT
25
* Average travel speed approximated from reported travel time measurements. Estimate includes intersection delay and transit dwell time.
AM Peak
PM Peak
Notes: Existing LOS AM/PM
Pie chart summarizing AM / PM - # of intersections in each category.
Key for coloring of circles.

## Slide 21: Defining Two Build Alternatives

## Slide 22: Define the Build Alternatives
Transitway entrance and exit locations
Existing bus routes and stop locations
Location of bus stops
Balance signal priority with safety and operations
Minimize increases in travel times
Removal of service lanes
Plan for loading and unloading zones
Mitigate turning conflicts with pedestrians
Safety and accessibility along corridor
Transitway access
Protection from right-turn conflicts
Accommodate crossing of K Street NW within a single signal cycle
Dedicated bicycle facility
Connection to existing and planned north-south bicycle facilities connected to K Street NW

## Slide 23
Alternative 1
Consolidated entry/exit points for transit
Reduced number of general purpose traffic lanes
Increased loading/unloading zones on K Street NW
Minimal changes to existing bus routes
Preservation of general purpose traffic lanes
Limited loading/unloading zones on K Street NW
Alternative 2
Dedicated, center-running transitway with five transit stops
Dedicated bike facilities in the median
Left turns restricted
Both
Define the Build Alternatives

## Slide 24: K Street NW Design Alternatives
Platform and Median (not all blocks)
Dedicated Bus Lanes
Protected Bike Lanes
Variable
Width
Median
1 through lane and 1 shared through and right-turn lane
2 through travel lanes (1 through lane and 1 shared through and right-turn lane)
Alternative 1
1 through travel lane and
1 dedicated right-turn lane
1 through travel lane and 1 curb lane -- varied use as turn lane or loading
Alternative 2

## Slide 25: K Street NW Design Alternatives
Alternative 1
Transitway
Intersections
Intersection Configurations
Alternative 2

## Slide 26: Transitway Access Options
Alternative 1
30s1
D6
21st
20th
19th
18th
CT
17th
16th
15th
VT
14th
13th
12th
11th
10th
30s1
K STREET NW TRANSITWAY
G8
G8
3Y
16Y
3Y
16Y
X2
80
G8
X2
80
G8
30s1
30s1
D6
X2
80
3Y
16Y
D6
X2
80
3Y
16Y
D6
22nd
30s1
30s1
3Y
16Y
30s1
3Y
16Y
3Y
16Y
80
G8
3Y
16Y
80
G8
X2
D6
21st
20th
19th
18th
CT
17th
16th
15th
VT
14th
13th
12th
11th
22nd
D6
D6
X2
80
D6
X2
80
10th
30s1
X2
K STREET NW TRANSITWAY
G8
G8
Alternative 2
Alternative 1 introduces more access points on and off the transitway on the west end of the network
Alternative 2 adjusts bus routing on the east end of the corridor to increase the number of buses utilizing the full transitway
Eastbound Westbound
130N, 30S, 32, 33, 36, 37, 39
Route Origin
Route Destination
USGT Circulator
Transitway
Transitway Entrance Only
Transitway Exit Only
Transitway Entrance/Exit
5 Entry/Exit Locations
4 Entry and 3 Exit Locations

## Slide 27
Bus Stop Locations on K Street Transitway
Average Dwell Time
16 sec
EASTBOUND
AM Peak
PM Peak
16 sec
WESTBOUND
Average Dwell Time
16 sec
AM Peak
PM Peak
16 sec
Hot Spots with High Average Dwell Time
K+CT, EB
30 sec
AM Peak
25 sec
AM Peak
K+CT, WB
K+19th
K+CT
K+16th
K+14th
K+13th
Notes:
Transit dwell time distributions for build conditions were derived from existing conditions dwell time distributions and reduced to reflect level-boarding, all-door boarding/alighting. The dwell time distributions were adjusted, this slide shows the resulting average dwell time.
The same reduced dwell-time distributions were applied in both alternatives.
Bus routes and schedules were adjusted in each build alternative according to the designated transitway entry and exit locations.
Due to these changes, more buses stop at each transitway stop as compared to individual stops in Existing Conditions and only WMATA and DC Circulator buses are allowed on the transitway. This contributes to the reported average dwell time.
PM peak period average dwell times were consistent with one another; hot spots were not identified.
Bus Dwell Time Assumptions

## Slide 28: Alternatives Analysis
Based on the poor performance of the PM peak period microsimulation model, the project team made the decision not to evaluate the AM peak period for Alternative 2

## Slide 29: Travel Time
AM Peak
PM Peak
6:16
--
6:34
9:06
--
9:45
7:54
--
8:09
9:06
--
9:32
EASTBOUND
Alt 1
Alt 2*
Alt 1
Alt 2*
Alt 1
Alt 2*
Alt 1
Alt 2*
WESTBOUND
AM Peak
PM Peak
Chart: 
| PM | AM | PM | AM
Alt 2 | 0.39792 | 0 | 0.59514 | 0
Alt 1 | 0.39722 | 0.41597 | 0.33958 | 0.32917
Existing | 0.58542 | 0.52153 | 0.40069 | 0.30625
Chart: 
| PM | AM | PM | AM
Alt 2 | 0.39653 | 0 | 0.59097 | 0
Alt 1 | 0.40625 | 0.37917 | 0.27361 | 0.26111
Existing | 0.63056 | 0.53889 | 0.31458 | 0.29722
Existing
Alt 1
Alt 2*
* Alternative 2 analysis only performed for PM Peak Period
9:31
9:33
14:17
14:11
Notes: Alt 1:
Vehicles Alternative 1 Conditions AM – Average eastbound travel time = 6:16, Average westbound travel time = 7:54
Transit Alternative 1 Conditions AM – Average eastbound travel time = 9:06, Average westbound travel time = 9:59 (includes dwell time)
Vehicles Alternative 1 Conditions PM – Average eastbound travel time = 6:34, Average westbound travel time = 8:09
Transit Alternative 1 Conditions PM – Average eastbound travel time = 9:45, Average westbound travel time = 9:32 (includes dwell time)
Alt 2:
Vehicles Alternative 2 Conditions AM – Average eastbound travel time = NA, Average westbound travel time = NA
Transit Alternative 2 Conditions AM – Average eastbound travel time = NA, Average westbound travel time = NA (includes dwell time)
Vehicles Alternative 2 Conditions PM – Average eastbound travel time = 14:11, Average westbound travel time = 14:17
Transit Alternative 2 Conditions PM – Average eastbound travel time = 9:31, Average westbound travel time = 9:33 (includes dwell time)

## Slide 30: Intersection Delay
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
Connecticut Avenue NW
Alternative 2*
Good
Poor
AM
PM
* Alternative 2 analysis only performed for PM Peak Period
Existing
Alternative 1

## Slide 31
K Street NW and
Connecticut Avenue NW
AM
PM
AM
PM
AM
PM
K Street NW and
Connecticut Avenue NW
AM
PM
AM
PM
AM
PM
K Street NW and
Connecticut Avenue NW
PM
PM
PM
Alternative 1
Alternative 2*
Existing
Approach Delay
K Street NW and
21st Street NW
AM - ML
PM - ML
AM
PM
AM
PM
AM
PM
AM - SL
PM - SL
ML: Mainline K Street NW (from tunnel) SL: Service Lane (from Washington Circle)
K Street NW and
21st Street NW
AM - ML
PM - ML
AM
PM
AM
PM
AM
PM
AM - SL
PM - SL
K Street NW and
21st Street NW
PM - ML
PM
AM
PM
PM
PM - SL
21st Street
Connecticut Ave
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor
AM
PM
Intersection Performance
Approach Performance
AM
PM
* Alternative 2 analysis only performed for PM Peak Period

## Slide 32
Alternative 1
Alternative 2*
Existing
K Street NW and
15th Street NW (west)
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
Vermont Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
15th Street NW (west)
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
Vermont Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
15th Street NW (west)
PM
PM
PM
PM
K Street NW and
Vermont Avenue NW
PM
PM
PM
PM
15th Street
Vermont Ave
* Alternative 2 analysis only performed for PM Peak Period
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor
AM
PM
Intersection Performance
Approach Performance
AM
PM
Approach Delay

## Slide 33
Alternative 1
Alternative 2*
Existing
K Street NW and
14th Street NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
12h Street NW
AM
PM
AM
PM
AM
PM
K Street NW and
14th Street NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
12h Street NW
AM
PM
AM
PM
AM
PM
K Street NW and
14th Street NW
PM
PM
PM
PM
K Street NW and
12h Street NW
PM
PM
PM
14th Street
12th Street
* Alternative 2 analysis only performed for PM Peak Period
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor
AM
PM
Intersection Performance
Approach Performance
AM
PM
Approach Delay

## Slide 34
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Connecticut Avenue NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
AM Peak
* Average travel speed approximated from reported travel time measurements. Estimate includes intersection delay and transit dwell time.
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
Connecticut Avenue NW
6 mph
7 mph
4 mph
4 mph
6 mph
6 mph
4 mph
SPEED LIMIT
25
Alternative 1
Alternative 2*
Existing
8 mph
6 mph
5 mph
6 mph
6 mph
5 mph
10 mph
6 mph
6 mph
6 mph
2 mph
2 mph
5 mph
Slowest Speeds along Corridor
* Alternative 2 analysis only performed for PM Peak Period
AM Peak
PM Peak
Notes: Existing LOS AM/PM
Pie chart summarizing AM / PM - # of intersections in each category.
Key for coloring of circles.

## Slide 35
Pros and Cons for Both Alternatives 1 & 2
Center-running exclusive transitway for WMATA & DC Circulator buses
Center-running dedicated bicycle lanes
Safety benefits from restricted left-turns on K Street NW
Removal of K Street NW service lanes
Right-in/right-out access at all existing alleys and garages
Rerouted left-turning movements to parallel facilities
Additional travel time delay for rerouted left-turns (note that existing peak period operations restrict left turns at most intersections)
Removal of K Street NW service lanes results in reduced curb space for loading and unloading
PROS
CONS
Alternative 1
Alternative 2

## Slide 36
Minimal impact to existing bus routes by allowing transitway entry and exit at 5 intersections
Transit travel time improvements (-20% to -36%) compared to existing
In most cases vehicle travel time improvements:
  AM eastbound: -12%
  AM westbound: -13%
  PM eastbound: -15%
Pros
Cons
Alternative 1
Slight increase in vehicle travel time in one direction:
  PM westbound: +7%
Transitway entry and exit design limits transit travel time reductions in the westbound direction
Limited right-of-way at Farragut Square for two through lanes
Limited curb space for loading and unloading
Minimal impact to existing bus routes by allowing transitway entry and exit at 5 intersections
Transit travel time improvements (-20% to -36%) compared to existing
In most cases vehicle travel time improvements:
  AM eastbound: -12%
  AM westbound: -13%
  PM eastbound: -15%
Modest increase in vehicle travel time in one direction:
  PM westbound: +7%
Limited right-of-way at Farragut Square for two through lanes
Limited curb space for loading and unloading
Added transitway exit locations (19th Street NW and 20th Street NW) limits transit travel time reductions in the westbound direction
PROS
CONS
Pros and Cons Specific to Alternative 1

## Slide 37
Constructible cross-section based on right-of-way constraints at Farragut square
Increased curb space for loading and unloading
Introduced dedicated eastbound right-turn lane at 19th Street NW
Streamline transitway performance by only allowing transitway entry and exit at 3 intersections
Transit travel time improvements (-32% to -37%) compared to existing (PM only)
Pros
Cons
Alternative 2
Through-vehicle demand for K Street NW during the PM peak is too high for a single lane to service
Route impacts to existing bus routes based on limited transitway access
The observed increase of vehicle travel time compared to existing (+49% to +88%) does not account for the high unserved demand of 25% (i.e., vehicles unable to make their trip during the peak period)
Transitway performance also impacted by vehicular delay, limiting signal timing optimization options and increasing incurred delay of buses prior to entering the transitway.
Transit travel time improvements (-32% to -37%) compared to existing (PM)
Constructible cross-section based on right-of-way constraints at Farragut square
Increased curb space for loading and unloading
Introduced dedicated eastbound right-turn lane at 19th Street NW
Streamline transitway performance by only allowing transitway entry and exit at 3 intersections
Through-vehicle demand for K Street NW during the PM peak is too high for a single lane to service
Greater bus route impacts to existing bus routes with limited transitway access points
The observed increase of vehicle travel time compared to existing (+49% to +88%) does not account for the high unserved demand of 25% (i.e., vehicles unable to make their trip during the peak period)
Transitway performance also impacted by vehicular delay, limiting signal timing optimization options and increasing incurred delay of buses prior to entering the transitway
PROS
CONS
Pros and Cons Specific to Alternative 2

## Slide 38: Development of the Hybrid Alternative

## Slide 39: Hybrid Alternative Design
Transitway
Hybrid Design
Westbound Approach – Alt 1
Eastbound Approaches – Alt 2
Alt 1 Design
Alternative 2
Alternative 1

## Slide 40: Hybrid Alternative Design
Lane Drop
Lane Drop
22nd
21st
20th
19th
18th
17th (E)
16th
15th (W)
VT
22nd
21st
20th
19th
18th
17th (W)
17th (E)
16th
15th (W)
15th (E)
14th
13th
12th
11th
10th
14th
13th
12th
11th
10th
CT
Legend: Center Line Transitway Stop Direction of Cross Street Transit Lane
Bike Lane Travel Lane Service Lane

## Slide 41: 1100-1200 Block of K Street NW
N
NOT TO
SCALE
30% design for eastern terminus of Transitway at 12th Street NW

## Slide 42: 1100-1200 Block of K Street NW
Alternate design for eastern terminus of Transitway at 12th Street NW
Eastbound buses and bicycles operate at the same time during a dedicated queue jump phase
Dedicated transitway entry lane for westbound buses
Dedicated eastbound right-turn lane allows for overlap signal operations, providing additional green time for turning buses
Westbound bicycles operate during the eastbound queue jump phase
Westbound buses operate concurrently with general purpose traffic and during the eastbound queue jump phase
N
NOT TO
SCALE

## Slide 43: 2000-2100 Block of K Street NW
30% design for western terminus of Transitway at 21st Street NW
N
NOT TO
SCALE

## Slide 44: 2000-2100 Block of K Street NW
Alternative design for western terminus of Transitway at 21st Street NW – Eastbound Option 2
Rush-hour restricted transit-only queue jump lane; optional curbside parking lane outside rush hour
Transitway entrance dwell area
Adjust service lane stop bar location
Moving the transitway dwell area to the curb positions the bus in an expected location and eliminates a potential sight distance obstruction for permissive westbound left-turning buses (see later exhibit)
Transit-only travel lane
Transit vehicle travel path (transition to/from the Transitway)
Element of Design Option
Benefit of Design Option
Shift in eastbound transitway entry lane to accommodate alternative design for westbound exit (see later exhibit)
N
NOT TO
SCALE

## Slide 45: Hybrid Alternative Performance

## Slide 46: Travel Time
AM Peak
PM Peak
7:33
9:25
EASTBOUND
Exist.
Hybrid
WESTBOUND
AM Peak
PM Peak
7:08
6:01
12:56
8:07
15:08
8:29
9:37
6:40
7:21
6:09
12:31
8:01
14:03
7:35
Existing
Hybrid
Exist.
Hybrid
Exist.
Hybrid
Exist.
Hybrid
Chart: 
| AM | PM | AM | PM
Hybrid | 0.35347 | 0.33819 | 0.39236 | 0.25069
Existing | 0.63056 | 0.53889 | 0.31458 | 0.29722
Chart: 
| AM | PM | AM | PM
Hybrid | 0.33403 | 0.31597 | 0.25556 | 0.27778
Existing | 0.52153 | 0.58542 | 0.30625 | 0.40069
Notes: Alt 1:
Vehicles Alternative 1 Conditions AM – Average eastbound travel time = 6:16, Average westbound travel time = 7:54
Transit Alternative 1 Conditions AM – Average eastbound travel time = 9:06, Average westbound travel time = 9:59 (includes dwell time)
Vehicles Alternative 1 Conditions PM – Average eastbound travel time = 6:34, Average westbound travel time = 8:09
Transit Alternative 1 Conditions PM – Average eastbound travel time = 9:45, Average westbound travel time = 9:32 (includes dwell time)
Alt 2:
Vehicles Alternative 2 Conditions AM – Average eastbound travel time = NA, Average westbound travel time = NA
Transit Alternative 2 Conditions AM – Average eastbound travel time = NA, Average westbound travel time = NA (includes dwell time)
Vehicles Alternative 2 Conditions PM – Average eastbound travel time = 14:11, Average westbound travel time = 14:17
Transit Alternative 2 Conditions PM – Average eastbound travel time = 9:31, Average westbound travel time = 9:33 (includes dwell time)

## Slide 47: Intersection Delay
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
Connecticut Avenue NW
Hybrid Alternative
Good
Poor
AM
PM
Existing

## Slide 48: Approach Delay
K Street NW and
Connecticut Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
15th Street NW (west)
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
Connecticut Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
Existing
K Street NW and
21st Street NW
AM - ML
PM - ML
AM
PM
AM
PM
AM
PM
AM - SL
PM - SL
K Street NW and
15th Street NW (west)
AM
PM
AM
PM
AM
PM
AM
PM
21st Street
CT Avenue
15th Street
Hybrid Alternative
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor
AM
PM
Intersection Performance
Approach Performance
AM
PM
K Street NW and
21st Street NW
AM - ML
PM - ML
AM
PM
AM
PM
AM
PM
AM - SL
PM - SL

## Slide 49: Approach Delay
K Street NW and
Vermont Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
14th Street NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
12h Street NW
AM
PM
AM
PM
AM
PM
K Street NW and
Vermont Avenue NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
14th Street NW
AM
PM
AM
PM
AM
PM
AM
PM
K Street NW and
12h Street NW
AM
PM
AM
PM
AM
PM
VT Avenue
14th Street
12th Street
Hybrid Alternative
Existing
0-35 Seconds of Delay
35-55 Seconds of Delay
55-80 Seconds of Delay
80+Seconds of Delay
Good
Poor
AM
PM
Intersection Performance
Approach Performance
AM
PM

## Slide 50: Slowest Speeds along Corridor
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Connecticut Avenue NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
AM Peak
* Average travel speed approximated from reported travel time measurements. Estimate includes intersection delay and transit dwell time.
22nd Street NW
21st Street NW
20th Street NW
19th Street NW
18th Street NW
13th Street NW
12th Street NW
11th Street NW
10th Street NW
9th Street NW
Vermont Avenue NW
17th Street NW
16th Street NW
15h Street NW
14th Street NW
Connecticut Avenue NW
6 mph
7 mph
4 mph
4 mph
6 mph
Hybrid Alternative
Existing
9 mph
6 mph
5 mph
5 mph
AM Peak
PM Peak
8 mph
5 mph
SPEED LIMIT
25
6 mph
4 mph
6 mph
7 mph
7 mph
Notes: Existing LOS AM/PM
Pie chart summarizing AM / PM - # of intersections in each category.
Key for coloring of circles.

## Slide 51: Pros and Cons of Hybrid Alternative
Constructible cross-section based on right-of-way constraints at Farragut square
Streamline transitway performance by only allowing transitway entry at 4 intersections and exit at 3 intersections
Transit travel time improvements (-36% to -46%) compared to existing
In most cases vehicle travel time improvements:
  AM eastbound: -16%
  PM eastbound: -17%
  PM westbound: -31%
Limited curb space for loading and unloading
Minor route changes to existing bus routes based on limited transitway access
Eastbound lane drop at 13th Street NW limits vehicular capacity and increases travel time.
  PM eastbound: +25%
PROS
CONS

## Slide 52: Next Steps

## Slide 53
Recommendation: Hybrid Alternative
1 Approximated travel time savings for a single peak period considering an average of 55 buses per hour and 11 riders per bus; average bus occupancy from WMATA AVL data.
36% to 46% Bus Travel Time Reduction
101 hours of travel time savings per peak period1
Minimal Impact to Vehicles
Similar driving experience as K Street NW today
New Protected Bike Facility
Favorable signalization alongside transitway
Improves connectivity of bicycle network
Safety risk reduced

## Slide 54
Path Forward
Design modifications at 21st Street NW and the 2000-2100 Block of K Street NW
Further optimization of transitway entry and exit design and signal operations
Consideration of removal of 1200 block transit stop
Consideration of impact on parallel facilities
Bus schedule review to consider headway-based entry to the transitway
Implement all-door bus boarding and alighting
3
2
1
4
5
6